Operational State
This illustrates a possible setup of eight Hermes Connect units, along with an extra. There are three uplinks shown. One is inband with the traffic in the cabinet (“core switch”), a second one utilities a commodity LTE gateway that provides NAT44 (maybe even CGN) access.
Also shown is a third uplink (“colo”) which provides services to many cabinets.
- All traffic between Connect units is encrypted, even with the cabinet.
- The green cables could be unencrypted IPMI cables, and the purple cables are RS232 serial console cables.

---
Technical details/Standards
- New units auto enroll using ANIMA bootstrap mechanism.
- Connect cables in any desired way, use as many hubs, switches or WAN links as desired.
- Access to serial port is via rfc2217 using ssltelnet, can be be kerberized. (or via ssh)
- ANIMA ACP uses auto configured IPsec/IKEv2 for traffic.
- ACP uses RPL (RFC6550) L3 routing protocol for (redundant) connectivity.
- RPL finds shortest path and keeps redundant paths available.